## Slide 1: PT statistics for small number of participants (Annex D of ISO 13528) S.SUBRAMANIAN

## Slide 2
When the number of participants “p” is less Assigned Value (and its uncertainty) and/or SDPA should be determined independent of the participants.
Possible methods for determination of Assigned Value and its uncertainty, as specified in clauses 7.3, 7.4, 7.5, or 7.6 of ISO 13528:2022 :
By formulation (Known Value Scheme) – clause 7.3;
By using a CRM as PT item - clause 7.4;
By characterizing the PT item using a valid CRM in one laboratory (also called as Value transfer from a CRM to a closely matched candidate RM) - clause 7.5;
Using consensus value from expert laboratories (which are not participants in the PT Scheme) - clause 7.6

## Slide 3
Possible methods for determination of Assigned Value and its uncertainty, as specified in clauses 8.2, 8.3, 8.4, or 8.5 of ISO 13528:2022 :
By perception of experts - clause 8.2;
By experience from previous rounds of a PT Scheme - clause 8.3;
By using Horwitz formula (applicable to analytical PT Schemes) - clause 8.4;
By using Reproducibility and/or Repeatability SD (as given in the standard test method) - clause 8.5.
By using this approach (determination of Assigned Value as well as SDPA independent of participants) PT Schemes can be conducted even with one participant .

## Slide 4
What to do when assigned value (and its uncertainty) can’t be determined independent of participants?
(e.g) Mechanical testing of textiles, leather etc., for tensile strength, GSM, Tear strength, Abrasion resistance etc., for which suitable CRMs are not available
Chemical testing of many products including textiles, (Shrinkage, Blend composition, Colour Fastness to laundering, dry cleaning, light, etc.,)
Only consensus value from the participants’ results can be used in such PT schemes.

## Slide 5
Robust estimators such as Algorithm A and nIQR method are used for the determination of both assigned value as well as SDPA while using consensus value from the participants’ results.
But, use of robust estimators are acceptable only when the number of participants (after removal of outliers) is ≥ 12.
In this case, the approach as specified in Annex D of ISO 13528:2022 can be used

## Slide 6: Annex D approach when “p” is < 12
Step 1: Identify outliers (blunders) in the participants results and remove them for determination of Assigned Value (and its uncertainty) as well as SDPA.
Step 2: Determine Assigned Value and its uncertainty from the participants’ results.
Step 3: Determine SDPA independent of participants, as given in clauses 8.2, 8.3, 8.4 or 8.5 of ISO 13528:2022. Alternatively, determine SDPA from the participants’ results using formula given below.
Step 4: Ensure that the performance of (outliers/ blunders) identified as per step-1 is not satisfactory. If it is not so, don’t consider such result as blunder and go to step-2.

## Slide 7: Annex D approach when “p” is < 12
Step 1: Identify outliers in the participants results and remove them for determination of Assigned Value (and its uncertainty) as well as SDPA.
Grubbs’ test
Using median & MPE
Results with Z/Z’ score 5 and below or 5 and above

## Slide 8: Annex D approach when “p” is < 12
Step 2: Determine Assigned Value and its uncertainty from the participants’ results.
Take the median of the participants’ results after removal of blunders as the Assigned Value. Also calculate standard deviation (SD)of the participants’ results.
Calculate the Standard Uncertainty in the assigned value, SU using the following formula:
SU = SD/√p
This method is valid only when the assigned value is validated by comparing the median of small number of participants with an independent reference value (such as homogeneity average value) as per clause 7.8 of ISO 13528:2022.

## Slide 9: Annex D approach when “p” is < 12
Step 3: Determine SDPA independent of participants, as given in clauses 8.2, 8.3, 8.4 or 8.5 of ISO 13528:2022. Alternatively, determine SDPA from the participants’ results using formula given below.
This method is valid only when Lower and Upper limit are stipulated for the SDPA determined from the participants’ results in accordance with Clause 8.6.2.1 and 8.6.2.2 of ISO 13528:2022.
SDPA = | Sum of absolute difference between each result and MEDIAN
 | (0.798 x p)

## Slide 10: Annex D approach when “p” is < 12
Step 4: Ensure that the performance of (outliers/ blunders) identified as per step-1 is not satisfactory. If it is not so, don’t consider such result as blunder and go to step-2.
i.e Do not consider such a result as blunder which is identified earlier as a blunder by Grubbs’ test or other means, but performance is not “unsatisfactory”. Recalculate both assigned value as well as SDPA by including the lab result which was originally identified as blunder.

## Slide 11: Annex D approach when “p” is < 12 SDPA determined using formula given in Annex D
 | Code |  | Value | Deviation | Z' Score
 | LAB-08 |  | 240 | 33.00 | -1.22
 | LAB-07 |  | 267 | 6.00 | -0.22
 | LAB-11 |  | 269 | 4.00 | -0.15
 | LAB-13 |  | 270 | 3.00 | -0.11
 | LAB-09 |  | 272 | 1.00 | -0.04
 | LAB-12 |  | 274 | 1.00 | 0.04
 | LAB-14 |  | 295 | 22.00 | 0.81
 | LAB-05 |  | 300 | 27.00 | 1.00
 | LAB-04 |  | 314 | 41.39 | 1.53
 | LAB-01 |  | 341 | 68.00 | 2.51
Assigned Value |  |  | 273.00 |  | 
p |  |  | 10 |  | 
 |  | AV= | 273.00 |  | 
 |  | SD= | 25.8634 |  | 
 |  | SU= | 8.1787 |  | 
 |  | 0.3 x SD= | 7.7590 |  | 

## Slide 12: Annex D approach when “p” is < 12 SDPA determined by perception – Clause 8.2
 | Code | Value | Deviation | Z' (from Deviation) | Z' @ 10%
 | EO_01 | 60.1 | 21.90 | -1.80 | -2.22
 | EO_13 | 79.8 | 2.20 | -0.18 | -0.22
 | EO_28 | 84.2 | 2.20 | 0.18 | 0.22
 | EO_14 | 90.5 | 8.50 | 0.70 | 0.86
Assigned Value |  | 82.00 |  |  | 
p |  | 4 |  |  | 
 | AV= | 82.00 |  |  | 
 | SD= | 10.902 | 13.295% | 8.20 | 
 | SU= | 5.451 |  |  | 
 | 0.3 x SD= | 2.460 |  |  |